## Slide 1: Bluetooth OBD-II Diagnostic Tool
Zak Rowland

## Slide 2: System block diagram

## Slide 3: System functionality
The ESP32 microcontroller interfaces with an ELM327 OBD-II interpreter
  The ESP32 writes commands and reads data through a wired serial connection
A Bluetooth connection between the Raspberry Pi 4 and the ESP32 will allow the user of the Raspberry Pi to interface with a vehicle wirelessly
  The Raspberry Pi will utilize Python scripts to communicate data and build a GUI
The Raspberry Pi will be powered by a rechargeable battery and have its own touchscreen

## Slide 4: Hardware functionality
During the last design discussion, I mentioned issues with my UART data being incorrect
  I was decoding the data MSB first instead of LSB
  The UART1 pins on the ESP32 are not recommended for uses other than SPI
    Switched to UART0
Arduino Uno (5V)
ESP32 
(3.3V)

## Slide 5: Hardware functionality cont.
This is the “AT I” command sent from the ESP32 after 3.3V to 5V conversion
  Noisy, but the data is there
  If the ESP32 ground was also connected to the circuit, the line remained high (no data appeared)
Before – 3.3V
After – 5V

## Slide 6: Hardware functionality cont.
This is the ELM327’s response to the “AT I” command sent from the ESP32 after 5V to 3.3V conversion
  Noisy, but the data is there
Before – 5V
After – 3.3V
The last piece of hardware to implement is the ADC to the Raspberry Pi 4 to monitor battery voltage

## Slide 7: Software functionality
Establishing Bluetooth connection between the Pi and ESP32
  Understanding how Bluetooth Low Energy works
Uses GATT (Generic Attribute Profile) to define how devices transfer data using services and characteristics
One device acts as the GATT Server (ESP32) and the other acts as the GATT Client (RPi 4)
The characteristics within services contain data to read, and some can be written to, allowing bi-directional communication
learn.adafruit.com/introduction-to-bluetooth-low-energy/gatt

## Slide 8: Software functionality cont.
I will need a BLE service that contains two characteristics for TX and RX
  This will act as the wireless UART

## Slide 9: Software functionality cont.

## Slide 10: Software functionality cont.
Used an example included in the ESP-IDF extension to establish and test the Bluetooth connection
  With help from the examples, I need to setup my own UART service with TX and RX characteristics
  Then create a Python script for the Raspberry Pi to pair, connect, then read and write to the Bluetooth characteristics

## Slide 11: Changes
Switched from Raspberry Pi OS to Pi OS Lite
  Uses less CPU and memory, improving battery life and efficiency
  Strips away unnecessary features and services, reducing storage space and boot time
  Defaults to the command line, but GUI functionality can be added
  Using SSH
May switch to Arduino IDE or Bluetooth Classic if I can’t get BLE going
  More documentation, support, and examples
    Faster to implement
  ESP-IDF utilizes FreeRTOS for its Bluetooth implementation
    Need to research and learn about FreeRTOS

## Slide 12: Timeline
https://trello.com/b/57kp2fr0/zaks-senior-project